## Slide 1
Digital Fundamentals
Tenth Edition
Floyd
Combinational Logic Analysis
© 2008 Pearson Education

## Slide 2: In this chapter
Objectives
  Analysis of combinational logic
  Implementation of combinational logic
  NAND/NOR universal gates and applications

## Slide 3
In Sum-of-Products (SOP) form, basic combinational circuits can be directly implemented with AND-OR combinations if the necessary complement terms are available.
Combinational Logic Circuits

## Slide 4
An example of an SOP implementation is shown. The SOP expression is an AND-OR combination of the input variables and the appropriate complements.
Combinational Logic Circuits
SOP
DE
ABC
A
B
C
E
D
X = ABC
+ DE

## Slide 5
In a certain chemical-processing plant, a liquid chemical is used in a manufacturing process. The chemical is stored in three different tanks. A level sensor in each tank produces a HIGH voltage when the level of chemical in the tank drops below a specified point. Design a circuit that monitors the chemical level in each tank and indicates when the level in any two of the tanks drops below the specified point.
Example

## Slide 6
When the output of a SOP form is inverted, the circuit is called an AND-OR-Invert circuit. The AOI configuration lends itself to product-of-sums (POS) implementation.
An example of an AOI implementation is shown. The output expression can be changed to a POS expression by applying DeMorgan’s theorem twice.
Combinational Logic Circuits
POS
DE
ABC
A
B
C
E
D
X = ABC
+ DE
X = ABC
+ DE
X = (A + B + C)(D + E)
X = (ABC)(DE)
AOI
DeMorgan

## Slide 7
The sensors in the chemical tanks are being replaced by a new model that produces a LOW voltage instead of a HIGH voltage when the level of the chemical in the tank drops below a critical point. Modify the circuit to operate with the different input levels and still produce a HIGH output to activate the indicator when the level in any two of the tanks drops below the critical point. Show the logic diagram
Example

## Slide 8
The truth table for an exclusive-OR gate is
Exclusive-OR Logic
A
B
Notice that the output is HIGH whenever A and B disagree.
The Boolean expression is
The circuit can be drawn as
X
Symbols:
Distinctive shape Rectangular outline
X = AB + AB

## Slide 9
The truth table for an exclusive-NOR gate is
Exclusive-NOR Logic
A
B
Notice that the output is HIGH whenever A and B agree.
The Boolean expression is
The circuit can be drawn as
X
Symbols:
Distinctive shape Rectangular outline
X = AB + AB

## Slide 10
For each circuit, determine if the LED should be on or off.
(a) (b) (c)
Circuit (a): XOR, inputs agree, output is LOW, LED is ON.
Circuit (b): XNOR, inputs disagree, output is LOW, LED is ON.
Circuit (c): XOR, inputs disagree, output is HIGH, LED is OFF.
Example
Solution

## Slide 11
Use exclusive-OR gates to implement an even-parity code generator for an original 4-bit code.
Example

## Slide 12
Example
Use exclusive-OR gates to implement an even-parity checker for the 5-bit code generated by the circuit in the previous slides.

## Slide 13
Implementing a SOP expression is done by first forming the AND terms; then the terms are ORed together.
Implementing Combinational Logic
Example
Solution
Show the circuit that will implement the Boolean expression X = ABC + ABD + BDE. (Assume that the variables and their complements are available.)
C
A
B
E
D
B
A
B
D
Start by forming the terms using three 3-input AND gates.
Then combine the three terms using a 3-input OR gate.
X = ABC + ABD + BDE

## Slide 14
Example
Develop a logic circuit with four input variables that will only produce a 1 output when exactly three input variables are 1s

## Slide 15
Example
Reduce the combinational logic circuit to a minimum form
Solution

## Slide 16
For basic combinational logic circuits, the Karnaugh map can be read and the circuit drawn as a minimum SOP.
Karnaugh Map Implementation
Example
Solution
A Karnaugh map is drawn from a truth table. Read the minimum SOP expression and draw the circuit.
1. Group the 1’s into two overlapping groups as indicated.
Read each group by eliminating any variable that changes across a boundary.
B changes across this boundary
C changes across this boundary
The vertical group is read A C.
The horizontal group is read AB.
The circuit is on the next slide:

## Slide 17
Minimize the combinational logic circuit. Inverters for the complemented variables are not shown.
Example

## Slide 18
Solution

## Slide 19
Circuit:
C
A
A
C
A
+
A
B
Solution
continued…
X =
The result is shown as a sum of products.
It is a simple matter to implement this form using only NAND gates as shown in the text and following example.
B

## Slide 20
NAND Logic
Example
Convert the circuit in the previous example to one that uses only NAND gates.
Recall from Boolean algebra that double inversion cancels. By adding inverting bubbles to above circuit, it is easily converted to NAND gates:
C
A
B
A
C
A
+
A
B
X =
Solution
C
A
A
C
+
A
B
X =
B
A

## Slide 21
Recall from DeMorgan’s theorem that AB = A + B. By using equivalent symbols, it is simpler to read the logic of SOP forms. The earlier example shows the idea:
NAND Logic
C
A
B
A
C
A
+
A
B
X =
The logic is easy to read if you (mentally) cancel the two connected bubbles on a line.

## Slide 22
NAND gates are sometimes called universal gates because they can be used to produce the other basic Boolean functions.
Universal Gates
Inverter
A
A
AND gate
A
B
AB
A
B
A + B
OR gate
A
B
A + B
NOR gate

## Slide 23
NOR Logic
B
A
C
A
X =
Again, the logic is easy to read if you cancel the two connected bubbles on a line.
Alternatively, DeMorgan’s theorem can be written as A + B = A B. By using equivalent symbols, it is simpler to read the logic of POS forms. For example,
(A + B)(A + C)

## Slide 24
NOR gates are also universal gates and can form all of the basic gates.
Universal Gates
Inverter
A
A
OR gate
A
B
A + B
A
B
AB
AND gate
A
B
AB
NAND gate

## Slide 25: 5.4 Combinational Logic Using NAND and NOR Gates
How can NAND and NOR gates be used to implement a logic function?

## Slide 26: Figure 5–19 Development of the AND-OR equivalent of the circuit in Figure 5–18.

## Slide 27: Figure 5–18 NAND logic for X = AB + CD.

## Slide 28: Figure 5–20 Illustration of the use of the appropriate dual symbols in a NAND logic diagram.

## Slide 29: Figure 5–24 NOR logic for X = (A + B)(C + D).

## Slide 30: Example: Illustration of the use of the appropriate dual symbols in a NOR logic diagram.

## Slide 31: Example: Using appropriate dual symbols, redraw the logic diagram and develop the output expression for the circuit in the following figure.

## Slide 32: 5.5 Logic Circuit Operation with Pulse Waveform Inputs
The output of an AND gate is HIGH only when all inputs are HIGH at the same time;
The output of an OR gate is HIGH only when at least one of its inputs is HIGH;
The output of a NAND gate is LOW only when all inputs are HIGH at the same time;
The output of a NOR gate is LOW only when at least one of its inputs is HIGH.

## Slide 33
Pulsed Waveforms
For combinational circuits with pulsed inputs, the output can be predicted by developing intermediate outputs and combining the result. For example, the circuit shown can be analyzed at the outputs of the OR gates:
A
B
C
D
A
B
C
D
G1
G2
G3
G1
G2
G3

## Slide 34
Pulsed Waveforms
Alternatively, you can develop the truth table for the circuit and enter 0’s and 1’s on the waveforms. Then read the output from the table.
A
B
C
D
A
B
C
D
G1
G2
G3
G3
Inputs
A B C D
Output
0 0 0 0
0 0 0 1
0 0 1 0
0 0 1 1
0 1 0 0
0 1 0 1
0 1 1 0
0 1 1 1
1 0 0 0
1 0 0 1
1 0 1 0
1 0 1 1
1 1 0 0
1 1 0 1
1 1 1 0
1 1 1 1
0 1 0 1 0 1 0 1 0 1
0 1 1 0 0 1 1 0 0 0
0 0 0 1 1 1 1 0 0 0
0 0 0 0 0 0 0 1 1 0
0 0 0 0 1 1 1 0 1 0
X
0
1
1
1
0
1
1
1
0
0
0
0
0
1
1
1

## Slide 35: Example: Determine the final output waveform X for the circuit in the following figure, with input waveforms A, B, and C as shown.

## Slide 36
Example: Determine the final output waveform X for the circuit in the following figure, with input waveforms A, B, and C as shown.

## Slide 37
Example: Determine the final output waveform X for the circuit in the following figure, with input waveforms A, B, and C as shown.

## Slide 38
Example: Determine the final output waveform X for the circuit in the following figure, with input waveforms A, B, and C as shown.

## Slide 39
© 2008 Pearson Education
Quiz
1. Assume an AOI expression is AB + CD. The equivalent POS expression is
a. (A + B)(C + D)
b. (A + B)(C + D)
c. (A + B)(C + D)
d. none of the above

## Slide 40
2. The truth table shown is for
a. a NAND gate
b. a NOR gate
c. an exclusive-OR gate
d. an exclusive-NOR gate
© 2008 Pearson Education
Quiz

## Slide 41
3. An LED that should be ON is
a. LED-1
b. LED-2
c. neither
d. both
© 2008 Pearson Education
Quiz

## Slide 42
© 2008 Pearson Education
Quiz
4. To implement the SOP expression , the type of gate that is needed is a
a. 3-input AND gate
b. 3-input NAND gate
c. 3-input OR gate
d. 3-input NOR gate
X = ABC + ABD + BDE
C
A
B
E
D
B
A
B
D

## Slide 43
© 2008 Pearson Education
Quiz
5. Reading the Karnaugh map, the logic expression is
a. A C + A B
b. A B + A C
c. A B + B C
d. A B + A C

## Slide 44
6. The circuit shown will have identical logic out if all gates are changed to
a. AND gates
b. OR gates
c. NAND gates
d. NOR gates
© 2008 Pearson Education
Quiz
A
B
C
D

## Slide 45
7. The two types of gates which are called universal gates are
a. AND/OR
b. NAND/NOR
c. AND/NAND
d. OR/NOR
© 2008 Pearson Education
Quiz

## Slide 46
10. During the first three intervals for the pulsed circuit shown, the output of
a. G1 is LOW and G2 is LOW
b. G1 is LOW and G2 is HIGH
c. G1 is HIGH and G2 is LOW
d. G1 is HIGH and G2 is HIGH
© 2008 Pearson Education
Quiz
A
B
C
D
A
B
C
D
G1
G2
G3