## Slide 1: Chapter 9 Counters

## Slide 2: Outline
Asynchronous Counter Operation
Synchronous Counter Operation
Up/Down Synchronous Counters
Design of Synchronous Counters
Cascaded Counters
Counter Decoding
Counter Applications

## Slide 3: 9.1 Asynchronous Counter Operation (异步计数器)
Asynchronous
  Events do not have a fixed time relationship with each other
  Events do not occur at the same time
An asynchronous counter
  The Flip-flops within the counter do not change states at exactly the same time
  The Flip-flops within the counter do not have a common clock pulse

## Slide 4: A 2-bit Asynchronous Binary Counter

## Slide 5: A 3-bit Asynchronous Binary Counter

## Slide 6: Propagation Delay
Figure 8–4 Propagation delays in a 3-bit asynchronous (ripple-clocked) binary counter.

## Slide 7
A 4-bit asynchronous binary counter is shown in Figure 9–8(a). Each D flip-flop is negative edge-triggered and has a propagation delay for 10 nanoseconds (ns). Develop a timing diagram showing the Q output of each flip-flop, and determine the total propagation delay time from the triggering edge of a clock pulse until a corresponding change can occur in the state of Q3. Also determine the maximum clock frequency at which the counter can be operated.

## Slide 9: Asynchronous Decade Counters
Figure 8–6 An asynchronously clocked decade counter with asynchronous recycling.

## Slide 10: 74LS93

## Slide 11
Figure 8–9 Two configurations of the 74LS93 asynchronous counter.

## Slide 12
How to use 74LS93 as a modulus-12 counter?

## Slide 13
Figure 8–10 74LS93 connected as a modulus-12 counter.

## Slide 14: 9.2 Synchronous Counter Operation (同步计数器)
Synchronous
  Events have a fixed time relationship with each other
A synchronous counter
  All Flip-flops within the counter are clocked at the same time by a common clock pulse

## Slide 15: A 2-bit Synchronous Binary Counter
Figure 8–11 A 2-bit synchronous binary counter.

## Slide 16
Figure 8–12 Timing details for the 2-bit synchronous counter operation (the propagation delays of both flip-flops are assumed to be equal).

## Slide 17
Figure 8–13 Timing diagram for the counter of Figure 8–11.

## Slide 18
Figure 8–14 A 3-bit synchronous binary counter.

## Slide 20
What is the function of the counter below?

## Slide 21
Figure 8–17 A synchronous BCD decade counter.

## Slide 23
Figure 8–19 The 74HC163 4-bit synchronous binary counter.
: Goes High when the counter reaches the last state in its sequence of fifteen.
: Enable inputs
: Clear inputs (S)
: Load inputs (S)

## Slide 24
Figure 8–20 Timing example for a 74HC163.

## Slide 25: 9.3 Up/Down Synchronous Counters (加/减同步计数器)
Be capable of progressing in either direction through a certain sequence.
Also be called as a bidirectional counter

## Slide 26
CLOCK PULSE | UP | Q2 | Q1 | Q0 | DOWN
0 |  | 0 | 0 | 0 | 
1 |  | 0 | 0 | 1 | 
2 |  | 0 | 1 | 0 | 
3 |  | 0 | 1 | 1 | 
4 |  | 1 | 0 | 0 | 
5 |  | 1 | 0 | 1 | 
6 |  | 1 | 1 | 0 | 
7 |  | 1 | 1 | 1 | 
Up/Down sequence for a 3-bit binary counter

## Slide 27
Figure 8–23 A basic 3-bit up/down synchronous counter.

## Slide 28
Figure 8–25 The 74HC190 up/down synchronous decade counter (十进制计数器).
Produces a HIGH pulse when the terminal count nine (1001) is reached in the UP mode or when the terminal count zero (0000) is reached in the DOWN mode.
Count enable input
Ripple clock output

## Slide 29
Figure 8–26 Timing example for a 74HC190.

## Slide 30: 9.4 Design of Synchronous Counters
Moore circuits (摩尔型有限状态机)
  The output or outputs depend only on the present internal state

## Slide 31: Moore Machine

## Slide 32
Mealy circuits (米利型有限状态机)
  The output or outputs depend on both the present state and the input or inputs

## Slide 33: Mealy Machine

## Slide 35: A general design procedure for sequential circuits
State Diagram
Next-State Table
Flip-Flop Transition Table
Karnaugh Maps
Logic Expressions for Flip-Flop Inputs
Counter Implementation

## Slide 36
Example: Design of a basic 3-bit Gray code counter.
Step 1: State Diagram

## Slide 37
Step 2: Next-State Table
Present State |  |  | Next State |  | 
Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 1 | 1
0 | 1 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 0 | 1
1 | 0 | 1 | 1 | 0 | 0
1 | 0 | 0 | 0 | 0 | 0

## Slide 38
Step 3: Flip-Flop Transition Table
Output Transitions |  |  | Flip-Flop Inputs | 
QN |  | QN+1 | J | K
0 | → | 0 | 0 | X
0 | → | 1 | 1 | X
1 | → | 0 | X | 1
1 | → | 1 | X | 0
QN: present state |  |  |  | 
QN+1: next state |  |  |  | 
X: “don’t care” |  |  |  | 
Transition table for a J-K flip-flop

## Slide 39
Step 4: Karnaugh Map

## Slide 41
Step 5: Logic Expressions for Flip-Flop Inputs

## Slide 42
Step 6: Counter Implementation

## Slide 43
Example: Develop a synchronous 3-bit up/down counter with a Gray code sequence.
Step 1: State Diagram

## Slide 44
Step 2: Next-State Table
Present State |  |  | Next State |  |  |  |  | 
Q2 | Q1 | Q0 | Y=0 (DOWN) |  |  | Y=1 (UP) |  | 
 |  |  | Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 45
Step 3: Flip-Flop Transition Table
Output Transitions |  |  | Flip-Flop Inputs | 
QN |  | QN+1 | J | K
0 | → | 0 | 0 | X
0 | → | 1 | 1 | X
1 | → | 0 | X | 1
1 | → | 1 | X | 0
QN: present state |  |  |  | 
QN+1: next state |  |  |  | 
X: “don’t care” |  |  |  | 
Transition table for a J-K flip-flop

## Slide 46
Present State |  |  | Next State |  |  |  |  | 
Q2 | Q1 | Q0 | Y=0 (DOWN) |  |  | Y=1 (UP) |  | 
 |  |  | Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 0 | 1 | 0 | 0 | 0 | 0 | 1
0 | 0 | 1 | 0 | 0 | 0 | 0 | 1 | 1
0 | 1 | 1 | 0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 0 | 1 | 1 | 1 | 1 | 0
1 | 1 | 0 | 0 | 1 | 0 | 1 | 1 | 1
1 | 1 | 1 | 1 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1 | 1 | 0 | 0
1 | 0 | 0 | 1 | 0 | 1 | 0 | 0 | 0

## Slide 47
Step 4: Karnaugh Map

## Slide 48
Step 5: Logic Expressions for Flip-Flop Inputs

## Slide 49
Step 6: Counter Implementation

## Slide 50
Example
Solution
Design a counter with the following counting sequence:
001010101111001…
Current State |  |  | Next State |  | 
Q2 | Q1 | Q0 | Q2 | Q1 | Q0
0 | 0 | 1 | 0 | 1 | 0
0 | 1 | 0 | 1 | 0 | 1
1 | 0 | 1 | 1 | 1 | 1
1 | 1 | 1 | 0 | 0 | 1
(1) Determine the next state table

## Slide 51
(2) Find the K-maps for all J-K FFs

## Slide 52
(3) Draw the circuit

## Slide 53
(4) Check whether the circuit is able to self start (Optional)
Determine if the circuit is able to enter one of the desired states (in the state diagram) after a finite number of transitions.
If it can not, you may have to re-design the circuit.

## Slide 54: 9.5 Cascaded Counters
Connect counter to achieve higher-modulus operation
Cascading
  The last-stage output of one counter drives the input of the next counter

## Slide 55
Figure 8–38 Two cascaded counters (all J and K inputs are HIGH).

## Slide 56
Figure 8–40 A modulus-100 counter using two cascaded decade counters.

## Slide 59
Use 74HC190 up/down decade counters connected in the UP mode to obtain a 10 kHz waveform from a 1 MHz clock. Show the logic diagram

## Slide 60
Figure 8–43 A divide-by-100 counter using two 74F162 decade counters.

## Slide 61: Cascaded Counters with Truncated Sequences
Figure 8–44 A divide-by-40,000 counter using 74HC161 4-bit binary counters. Note that each of the parallel data inputs is shown in binary order (the right-most bit D0 is the LSB in each counter).

## Slide 62: 9.6 Counter Decoding

## Slide 63
Figure 8–45 Decoding of state 6 (110).

## Slide 64
Figure 8–46 A 3-bit counter with active-HIGH decoding of count 2 and count 7.

## Slide 65
Decoding Glitches

## Slide 67: 9.7 Counter Applications

## Slide 68
Figure 8–51 Simplified logic diagram for a 12-hour digital clock.

## Slide 69
Figure 8–52 Logic diagram of typical divide-by-60 counter using 74F162 synchronous decade counters. Note that the outputs are in binary order (the right-most bit is the LSB).
: Asynchronously reset the counter

## Slide 70
Figure 8–53 Logic diagram for hours counter and decoders. Note that on the counter inputs and outputs, the right-most bit is the LSB.
: Synchronously preset the counter

## Slide 71
Application 2: Automobile Parking Control

## Slide 73
Application 3: Parallel-to-Serial Data Conversion (Multiplexing)

## Slide 75: Summary
Asynchronous counter and synchronous counter
  concepts
Up/down synchronous counter
How to design a synchronous counter?
  methods
Cascaded counter
  methods
Applications

## Slide 76
1. The counter shown below is an example of
a. an asynchronous counter
b. a BCD counter
c. a synchronous counter
d. none of the above
© 2008 Pearson Education
Quiz
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH

## Slide 77
The Q0 output of the counter shown
a. is present before Q1 or Q2
b. changes on every clock pulse
c. has a higher frequency than Q1 or Q2
d. all of the above
© 2008 Pearson Education
Quiz
CLK
K0
J0
Q0
Q0
C
C
C
J1
J2
K1
K2
Q1
Q2
Q1
HIGH

## Slide 78
3. To cause a D flip-flop to toggle, connect the
a. clock to the D input
b. Q output to the D input
c. Q output to the D input
d. clock to the preset input
© 2008 Pearson Education
Quiz

## Slide 79
4. The 7493A asynchronous counter diagram is shown (J’s and K’s are HIGH.) To make the count have a modulus of 16, connect
a. Q0 to RO(1) and RO(2) to
b. Q3 to RO(1) and RO(2)
c. CLK A and CLK B together
d. Q0 to CLK B
Quiz
© 2008 Pearson Education

## Slide 80
© 2008 Pearson Education
Quiz
FF0
FF1
FF2
5. Assume Q0 is LOW. The next clock pulse will cause
a. FF1 and FF2 to both toggle
b. FF1 and FF2 to both latch
c. FF1 to latch; FF2 to toggle
d. FF1 to toggle; FF2 to latch
LOW

## Slide 81
© 2008 Pearson Education
Quiz
6. A 4-bit binary counter has a terminal count of
a. 4
b. 10
c. 15
d. 16

## Slide 82
© 2008 Pearson Education
Quiz
7. Assume the clock for a 4-bit binary counter is 80 kHz. The output frequency of the fourth stage (Q3) is
a. 5 kHz
b. 10 kHz
c. 20 kHz
d. 320 kHz

## Slide 83
8. A 3-bit count sequence is shown for a counter (Q2 is the MSB). The sequence is
a. 0-1-2-3-4-5-6-7-0 (repeat)
b. 0-1-3-2-6-7-5-4-0 (repeat)
c. 0-2-4-6-1-3-5-7-0 (repeat)
d. 0-4-6-2-3-7-5-1-0 (repeat)
© 2008 Pearson Education
Quiz
Q0
Q1
Q2

## Slide 84
9. FF2 represents the MSB. The counts that are being decoded by the 3-input AND gates are
a. 2 and 3
b. 3 and 6
c. 2 and 5
d. 5 and 6
© 2008 Pearson Education
Quiz

## Slide 85
10. Assume the input frequency (fin) is 256 Hz. The output frequency (fout) will be
a. 16 Hz
b. 1 kHz
c. 65 kHz
d. none of the above
© 2008 Pearson Education
Quiz
HIGH
CLK
Q0
Q1
Q2
C
Counter 1
Counter 2
C
CTEN
CTEN
CTR DIV 16
CTR DIV 16
Q3
Q0
Q1
Q2
Q3
TC
TC
fin
fout